## Slide 1: Austin Baseline Update
Lawrence Berkeley National Laboratory

## Slide 2: Overview: Status
Standalone BEAM/ActivitySim Calibration:
  Additional calibration completed and new outputs generated
  Temporary fix for car ownership mismatch completed, long-term solution identified
  Fixed issue with LDV energy consumption
  Still some improvements that can probably be made in terms of traffic speeds and walk mode
Pilates integration:
  Full set of tests complete and working as expected
  Launching (/just launched) set of demonstration Austin scenarios today
  Will allow us to better understand sensitivity of car ownership and mode split to congestion and pricing
Notes: R

## Slide 3: Overview: Calibration
Primary issues discovered last time
  Mode split: Too much walking (15% of trips)
  LDV energy consumption: Too low, too many EVs, RH fleet too inefficient
  Travel speeds: Too fast
Fixes made
  Mode split:
    Create (penalized) vehicle for car travelers so they are not stranded
    ActivitySim consortium is working on vehicle bookkeeping that will solve this
  LDV energy consumption:
    Better calibration of ride hail fleet size and repositioning
    Fixed file structure disconnect with RouteE
  Travel speeds:
    More car trips, additional calibration of traffic network parameters
Notes: R

## Slide 4: Overview: PILATES
Latest results
  ActivitySim-Light – Re-run subset of ActivitySim models between BEAM iterations to allow for mode choice to come to equilibrium as the traffic network does
    Every iteration, fewer agents change their mode within ActivitySim, meaning that they are settling on user equilibrium
    The BEAM skims change less every iteration, meaning that the system is settling on traffic equilibrium
  Full ActivitySim – Re-run all ActivitySim models in response to changes from UrbanSim
    With UrbanSim turned off, activity patterns also make smaller changes every iteration
    Can also allow for changes in vehicle ownership and commute distance
Next steps
  Scenario runs in Austin
    Change traffic congestion levels and transit prices, looking for changes in auto ownership, commute distance, and auto mode share
Notes: R

## Slide 5: Mode split results
Mode | Unit | POLARIS | BEAM | SURVEY | BEAM September | BEAM Latest
City |  |  |  |  |  | 
SOV | % | 82.14% | 85.21% | 80.25% | 53.7% | 51.5%
HOV | % | 10.50% |  | 11.34% | 12.2% | 29.0%
Transit | % | 1.96% | 2.35% | 1.70% | 6.0% | 5.6%
Walk | % | 3.63% | 1.92% | 4.84% | 10.3% | 9.5%
Taxi | % | 0.18% | 6.52% | 0.13% | 3.6% | 3.3%
Bike | % | 1.59% | 4.00% | 1.23% | 1.1% | 1.0%
Rest of the Region |  |  |  |  |  | 
SOV | % | 83.49% | 83.75% | 83.12% | 51.7% | 50.2%
HOV | % | 11.60% |  | 13.10% | 13.3% | 32.6%
Transit | % | 0.53% | 0.13% | 0.82% | 3.1% | 0.2%
Walk | % | 3.25% | 2.06% | 2.50% | 12.8% | 12.8%
Taxi | % | 0.21% | 7.21% | 0.03% | 3.3% | 3.3%
Bike | % | 0.92% | 6.86% | 0.41% | 0.9% | 0.8%

## Slide 6: Energy Consumption
 | Unit | POLARIS | BEAM | BEAM September | Latest BEAM
TOTAL Fuel | Mgal | 2.86 | 1.24 | 1.90 | 1.23
Auto | Mgal | 1.44 | 0.88 | 1.47 | 1.12
TNC | Mgal | 0 | 0.14 | 0.22 | 0.12
Freight | Mgal | 1.38 | --- | --- | 
Transit | Mgal | 0.04 | 0.21 | 0.21 | 0.21
TOTAL Electricity | MWhr | 307.02 | 18.15 | 2081.08 | 25.20
Auto | MWhr | 305.73 | 15.96 | 1813.43 | 22.57
TNC | MWhr | 1.29 | 2.18 | 267.65 | 2.63
Freight | MWhr | 0 | --- | --- | 
Transit | MWhr | 0 | --- | --- | 
Total Energy | GWhr | 96.73 | 41.38 | 65.22 | 41.24
Auto | GWhr | 48.99 | 29.50 | 50.50 | 37.31
TNC | GWhr | 0.12 | 4.82 | 7.66 | 3.93
Freight | GWhr | 46.34 | --- | --- | 
Transit | GWhr | 1.28 | 7.06 | 7.06 | 7.06
TOTAL Energy per mile per vehicle | kWh/mile | 2.04 | ﻿0.798 | --- | --
Auto | kWh/mile | 1.24 | 0.66 | 1.41 | 1.05
TNC | kWh/mile | 0.89 | 0.76 | 1.41 | 1.01
Freight | kWh/mile | 6.98 | --- | --- | 
Transit | kWh/mile | 8.54 | 9.00 | 9.00 | 9.00
TOTAL Travel Efficiency | MPGGE | 16.5 | ﻿41.84 | --- | 
Auto | MPGGE | 27.1 | 50.58 | 23.70 | 31.85
TNC | MPGGE | 37.9 | 43.79 | 23.63 | 33.13
Freight | MPGGE | 4.8 | --- | --- | 
Transit | MPGGE | 3.9 | 3.71 | 3.71 | 3.71

## Slide 7: Summary Results
 | Unit | POLARIS | BEAM | BEAM September | Latest BEAM
Total Trips | million trips | 7.6 |  |  | 
Total Trips (Freight) | million trips | 0.4 |  |  | 
Total Trips (Auto-based) | million trips | 5.1 | 4.62 | 4.00 | 4.02
Productive-miles of Travel | million miles | 55.3 | 52.9 | 45.90 | 44.75
Productive-hours of Travel | million hours | 2.26 | 2.79 | 2.46 | 2.43
Vehicle miles Traveled (Total & by Auto, TNC, Freight, Transit) | million miles | 46.4 | 51.4 | 41.42 | 39.50
Vehicle hours Traveled | million hours | 1.85 | 1.56 | 0.98 | 0.99
Average Vehicle Travel Speed | MPH | 25.8 | 32.8 | 42.20 | 40.05
Average Trip Speed | MPH | 25.1 | 19 | 18.66 | 18.44
Total Energy | GWh | 96.73 | 41.4 | 65.22 | 48.30
Travel Efficiency | prd.mi/KWh | 0.57 | 0.17 | 0.14 | 0.19
Per capita Person-miles of Travel | miles | 29.4 | 31.9 | 30.60 | 26.69
Per capita Person-hours of Travel | hours | 1.2 | 1.68 | 1.64 | 1.45
Per capita Vehicle Miles Traveled | miles | 24.6 | 31.5 | 27.61 | 24.03
Per capita Vehicle Hours Traveled | hours | 0.99 | 0.98 | 0.65 | 0.62